## Slide 1: Computer Networks X_400487
Lecture 2
Chapter 2: The Physical Layer
Lecturer: Jesse Donkervliet

## Slide 2: Layered architecture
A (layered) architecture makes the system easier to understand
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
Real-world networks do not exactly match this architecture
Q: Why do we use it?

## Slide 3: Layered architecture
A (layered) architecture makes the system easier to understand.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
You are here
signals
Real-world networks do not exactly match this architecture
Q: Why do we use it?

## Slide 4: From a service to a signal, and back again
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals

## Slide 5: How can we transport data?
Well-known mediums:
Copper cables
Optical fibers
Radio waves
Other possible of mediums:
Postal service (“snail mail”)
A truck full of SSD drives
Trained pigeons with USB drives attached to their feet
…
Q: Can you think of mediums used for computer networks?
A medium allows you to transport data from one place to another

## Slide 6: Digital Modulation
Q: How to communicate bit strings (e.g., 101011101) between computer systems?
Bits and Bytes
11010101
Waves and Signals
Bits and Bytes
11010101
Modulation
Demodulation
Put information onto a carrier signal
Extract information from a carrier signal

## Slide 7: Different channel, different properties
Bit rate Number of bits per second. Depends on protocol, channel bandwidth, and other factors.
Delay How long does it take a bit to get to the end?
Storage Capacity How many bits can the channel hold at once? Capacity Bit rate Delay
Error Rate (Noise, Attenuation) What is the probability of a bit flipping?
Q: Which properties are important for video on-demand?
Non-functional properties can enable new technologies!

## Slide 8: Physical Layer Lecture
Physical Properties of Different Mediums
Communication Speed Limits
Digital Modulation
Multiplexing

## Slide 9: Twisted pair
Commonly used for:
Telephone networks.
Wired LANs.
Example: Category 6 (“CAT 6”) cables. Some support 500 MHz bandwidth.
Q: Why are the wires twisted?
High bandwidth allows higher data rates
Q: What about the latency and error rate?

## Slide 10: Coaxial (“coax”) cable
Commonly used for:
Telephone networks
Cable television
Wired Metropolitan Area Networks (MANs).
Bandwidth in the order of GHz.

## Slide 11: Optical fiber
Commonly used for:
Long-distance network backbones.
Wired Metropolitan Area Networks (MANs).
High-performance LANs.
Bandwidth in the order of 100 GHz.
Fiber is becoming increasingly popular in multiple application domains

## Slide 12: Wireless transmission
Different frequencies means different properties.
Radiowave
  AM radio
  FM radio
Microwave
  Satellite dishes
Infrared
  Remote controls
Visible light
…
Example?
Q: Can you think of a (dis)advantage compared to wired transmission?

## Slide 13: Wireless transmission
Different frequencies means different properties.
Radiowave
  AM radio
  FM radio
Microwave
  Satellite dishes
Infrared
  Remote controls
Visible light
…

## Slide 14: Radio
AM radio
FM radio
Q: Can you think of (dis)advantages?
Both can travel reasonably long distances

## Slide 15: Microwave
Q: Can you think of (dis)advantages?
Needs line of sight

## Slide 16: Satellite Networks
Radio waves allow for high bit rates and have (relatively) low attenuation.
But sending signals to artificial satellites and back has significant latency!
Q: What are its properties?
Lower latency requires lower orbits requires
more satellites

## Slide 17: Physical Layer Lecture
Physical Properties of Different Mediums
Communication Speed Limits
Digital Modulation
Multiplexing

## Slide 18: Fundamental speed limits

## Slide 19: Properties of Waves
Q: What are properties of waves?
Properties:
Amplitude
Frequency
Phase
Q: Which properties can we modulate simultaneously?
Frequency and phase are not independent

## Slide 20: Nyquist’s theorem
Computing the maximum data rate for a noiseless channel
= maximum data rate
= bandwidth
= number of discrete signal levels
Measured in bits/s
Measured in Hz

## Slide 21: Nyquist’s theorem An intuition
101010101010101
11
00
01
10
For a binary signal, V=2

## Slide 22: Nyquist’s Theorem Example
Signal that uses 4 signal levels over a wired channel with 500kHz bandwidth
Q: Can we exceed the maximum Nyquist data rate? Under what assumptions does this model hold?

## Slide 24: Shannon’s theorem
In practice, noise reduces the maximum data rate.
The signal to noise ratio ( or SNR) is expressed in decibel. SNR of dB means
Q: Why use decibels?
I.e., Signal power is 10,000 times stronger than Noise power
Q: Should we reduce noise or increase bandwidth?
Shannon’s Theorem + signal attenuation  limited cable length

## Slide 25: Shannon’s Theorem Example
Consider the signal and channel from before (4 signal levels, 500kHz bandwidth). What happens if the SNR is 40dB?
Signal level not used!
,
,

## Slide 26: Physical Layer Lecture
Physical Properties of Different Mediums
Communication Speed Limits
Digital Modulation
Multiplexing

## Slide 27: Digital Modulation
Translating Between Bits and Signals
Key responsibility of the physical layer

## Slide 28: Digital Modulation
Q: How to communicate bit strings (e.g., 101011101) between computer systems?
Bits and Bytes
11010101
Waves and Signals
Bits and Bytes
11010101
Modulation
Demodulation
Put information onto a carrier signal
Extract information from a carrier signal

## Slide 29: Digital Modulation: Baseband Transmission

## Slide 30: Representing Bits Using Signals
Data
01100010
Q: Why send an approximation?
Q: How close must the approximation be?
An approximation of the original signal

## Slide 31: Baseband transmission
Idea: send signals that represent one or more bits.
Bit stream: 1 1 0 0 1
Non-Return to Zero:
Manchester encoding:
clock:
Q: Can you think of a problem with this approach?
+V
-V
+V
-V
XOR

## Slide 32: Baseband transmission
Non-Return to Zero has clock recovery problems.
Manchester encoding halves the available bandwidth.
Q: Can you think of a better solution?
Bit stream: 1 1 0 0 1
NRZ Invert:
+V
-V

## Slide 33: 4B/5B encoding
Use a translation table to map sequences of 4 data bits to 5-bit codewords.
0000
1111
1010
11110
11101
10110
Data
Codeword
Q: What are the (dis)advantages of this approach?
Q: Could we use a different mapping?

## Slide 34: Scrambling
XOR the data with a random bit sequence.
E.g., use sequence 1110101.
0001010
Codeword
1110101
11111111
Data
Sequence
XOR
Q: What are the (dis)advantages of this approach?

## Slide 35: Digital modulation: Passband transmission

## Slide 36: Passband transmission
Low-frequency signals not always practical.
Not practical for wireless channels:
Antenna size
Interference
  Noise
  Other channel users!
Q: Why not?

## Slide 37: Passband transmission
Solution: move from [0, B] Hz to [S, S+B] Hz.
The passband
Frequency can be 0 Hz
Minimum frequency of Hz

## Slide 38: Baseband, Passband, and Bandwidth*
*Analog bandwidth (Hz)
frequency
0Hz
Frequency band
Frequency band
Starts at 0Hz  Baseband
Starts above 0Hz  Passband
Bandwidth
Q: How to differentiate the bits in passband?

## Slide 39: Digital Modulation
0 1 0
Binary signal
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)
time 
…

## Slide 40: Sending multiple bits per symbol
Binary Phase Shift Keying (BPSK)
0
180
90
270
BPSK
2 symbols
1 bit/symbol
time 

## Slide 41: Sending multiple bits per symbol
time 
Quadrature Phase Shift Keying (QPSK)
QPSK
4 symbols
2 bit/symbol
0
180
90
270
01
11
10
00
01
11
10
00
Gray encoding
Every adjacent pair of symbols only differs by one bit

## Slide 42: Physical Layer Lecture
Physical Properties of Different Mediums
Communication Speed Limits
Digital Modulation
Multiplexing

## Slide 43: Multiplexing
Key concept: resource sharing

## Slide 44: Multiplexing
Sending multiple signals via a single medium
Signals
Medium
Medium
Signals
Medium
Mux/Demux
Q: Why (not) do this?
Recursive multiplexing

## Slide 45: Simplex and Duplex Channels
Simplex channels only allow data to pass through in one direction.
Duplex channels allow data to pass through in both directions at the same time.
Half-duplex channels allow data in both directions, but not at the same time.
Q: Can you think of a simple way to build a duplex channel?

## Slide 46: Frequency Division Multiplexing
All stations send at the same time, at different frequencies.
Frequency
A
B
C
A
B
C
Frequency
Frequency
Frequency
Signals at the same frequency interfere with each other
4G
ADSL
…

## Slide 47: Time Division Multiplexing
Stations take turns on a fixed schedule. Widely used in telephone/cellular systems
data
data
data
Guard time protects against small variations in timing
time 
Q: Why these gaps?
Q: How does each station know when to send?

## Slide 48: Code Division Multiplexing
Stations send at the same time, at the same frequency
Receiver figures out who sent what
If a station sends 1, the receiver computes 1
If a station sends nothing, receiver computes 0
If a station sends 0, the receiver computes -1
Also called “Code Division Multiple Access” (CDMA)

## Slide 49: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
1
0
1 -1 -1 1
-1 1 1 -1
A
A’s chip sequence
Inverted chip sequence

## Slide 50: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
1 -1 -1 1
-1 -1 1 1
1 -1 1 -1
-1 1 1 -1
A
B
C
1
0
1 1 -1 -1
-1 1 -1 1

## Slide 51: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
1 -1 -1 1
-1 -1 1 1
1 -1 1 -1
-1 1 1 -1
A
B
C
1
0
1 1 -1 -1
-1 1 -1 1
1
-
0

## Slide 52: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
1 -1 -1 1
A
B
C
-1 1 -1 1
1
-
0
0 0 -2 2

## Slide 53: Code Division Multiplexing
Stations send at the same time, at the same frequency.
Receiver figures out who sent what.
If a station sends 1, the receiver computes 1.
If a station sends nothing, receiver computes 0.
If a station sends 0, the receiver computes -1.
Also called “Code Division Multiple Access” (CDMA)

## Slide 54: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
A
B
C
1
-
0
0 0 -2 2

## Slide 55: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
A
B
C
1
-
0
0 0 -2 2
1 -1 -1 1
-1 -1 1 1
1 -1 1 -1
1
If a station sends 1, the receiver computes 1.

## Slide 56: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
A
B
C
1
-
0
0 0 -2 2
1 -1 -1 1
-1 -1 1 1
1 -1 1 -1
1
If a station sends nothing, the receiver computes 0.

## Slide 57: Code Division Multiplexing
Every bit is split into chips. Each station is assigned a chip sequence.
Also called “Code Division Multiple Access” (CDMA)
A
B
C
1
-
0
0 0 -2 2
1 -1 -1 1
-1 -1 1 1
1 -1 1 -1
1
If a station sends 0, the receiver computes -1.

## Slide 58: Code Division Multiplexing
Requirements:
Inner product of sequence with itself is 1 (e.g., )
All chip sequences are pairwise orthogonal (e.g., )
Also called “Code Division Multiple Access” (CDMA)

## Slide 59
Q: Differences Between FDM, TDM, CDM? Do they matter?

## Slide 60: How Does Static Multiplexing Affect Apps?
A, video
B, video
C, www
D, email
A
B
C
D
Inefficient resource usage

## Slide 61: How Does Static Multiplexing Affect Apps?
A
B
C
D
A
B
C
D
…
Video streaming no longer works

## Slide 62: Real-World Examples

## Slide 63: Internet over telephone system
Bandwidth bottleneck at twisted pair
Fiber
Twisted Pair
Q: Why not twisted pair?
Q: What happens here?
Backbone Network
End Office

## Slide 64: Local loop Digital Subscriber Lines
DSL broadband sends data over the local loop to the local office using frequencies that are not used for POTS.
Uses (Orthogonal) Frequency Division Multiplexing
Networks no longer used primarily for voice
POTS = Plain Old Telephone System

## Slide 65: Fiber to the Home
Fiber
Fiber
TDM
Backbone Network
Optical splitter/combiner
Uses Time Division Multiplexing for upstream data.
Modems have to request upstream slots.
Q: Can you think of a (dis)advantage of this approach?
Requesting slots improves efficiency. Similar to STDM
Shared channel. Home modems need to time carefully when to send

## Slide 66: SONET (Synchronous Optical NETwork)
Worldwide standard for carrying digital signals on optical trunks.
Uses Time Division Multiplexing An STS-1 line sends 810-byte frames every 125µs. (52Mbps) Time kept by a master clock. (A synchronous system.)
Uses Frequency Division Multiplexing Multiple STS-1 lines are combined on a single fiber to use the available bandwidth.

## Slide 67: SONET
Header (overhead) interleaved with data (SPE)
Every square is one byte
Bytes are sent left-to-right, top-to-bottom

## Slide 68: Physical Layer Summary
Different transmission mediums have different properties
Digital Modulation to translate bits to and from analog signals
Multiplexing to send multiple signals through one medium